## Slide 1: HP VEE Programming
By Chris Robinson
Product Manager of Data Acquisition at Amplicon Liveline

## Slide 2: The Rules for programming in HP VEE
There are only two major rules you have to learn with HP VEE:-
  How to connect the blocks together so that the data flows correctly, and the function blocks action in the correct order.
  Transactions: how to transfer data to and from HP VEE.

## Slide 3: Rule 1: How to Connect Blocks
THE TERMINALS (OR PINS):
Trigger input
Data In Result Out
Control In Error Out
Trigger output

## Slide 4: Connecting the terminals - In detail
Data inputs: HP VEE handles numerous data types, including waveforms, multi-dimensional arrays, and strings. The data always enters a box from the left.
Control inputs: These do not action the block, but alter something related to the block. E.g filename, print, or autoscale.
Trigger in: This does not have to be connected, but if connected means that the box only actions when there is a change of state on the terminal.
Trigger out: This goes high when the block has finished actioning, but only when the data sent out reaches a dead end.
Result out: This outputs data as soon as it can. This can sometimes be in the form of trigger signals (e.g. with if/then/else commands)
Error output: In many applications when talking to files or comms links, errors are likely, so can be used rather than feared.

## Slide 5: Rule 2: Transactions
Definition:
The method of transferring data to and from HP VEE.
Applies to:
RS232
GPIB (HPIB)
VXI
Files
Printers
DDE to Excel, Word etc
To/From Data sets
Does not Apply to:
Active X, ISA or PCI

## Slide 6: TRANSACTIONS - Step 1
Choose the appropriate transaction box from the I/O pull-down menu.
The example here is the “Direct I/O” transaction box from the “Instrument Manager” option in the I/O pull-down menu.


## Slide 7: TRANSACTIONS - Step 2
Add the correct terminals to the block by moving your mouse over the block (labelled here “serial(@ 9)”), pressing the right mouse button, and using the add terminal function.
Double click on the terminals to label them.
Any variable in a transaction refers to a terminal of the same name.

## Slide 8: TRANSACTIONS - Step 3
To add a transaction to the block:
double click in the white area in the middle.
The I/O transaction box will appear.
Select read or write and the most appropriate format, for the data, then press “OK” .
“Add Transaction” and “Delete Transaction” options can be seen when you do a right mouse click over the block.

## Slide 9: FINDING THE RIGHT FUNCTION.

## Slide 10: DIFFERENT WAYS TO CHOOSE A FUNCTION BLOCK
There are over 350 built in functions to choose from, these are the three main ways to find the right one.
From pull-down menus
  For most popular functions (explained later)
From “Device” menu
  A summary of functions can be found by selecting “Device”, then “Math & Functions”.
The Fx icon
  The shortcut to “Math & Functions” - There are five types of functions, for types of functions with a wide selection, there are often submenus.

## Slide 11: FUNCTION BLOCKS ACCESSABLE FROM PULL-DOWN MENUS
Flow:
For blocks that generate trigger signals:
  If/Then/Else
  OK button
  Repeat Until / Repeat for count
  Gates


## Slide 12: FUNCTION BLOCKS ACCESSABLE FROM PULL-DOWN MENUS
Device:
Function libraries, and Miscellaneous.
  Import libraries of special functions
  Select function from alphabetical list (using submenus)
  Blank “Formula” block
  Virtual function generators
  Sequencer


## Slide 13: FUNCTION BLOCKS ACCESSABLE FROM PULL-DOWN MENUS
Data:
Requesting, creating, or modifying data.
  Knobs and Sliders
  Selection controls
  Build or Un-build more complicated data types (such as Waveforms, Records or Datasets)
  Pop-up dialog boxes
  Blocks which connect together or build arrays


## Slide 14: FUNCTION BLOCKS ACCESSABLE FROM PULL-DOWN MENUS
Display:
Graphs and viewports
  Alphanumeric
  Strip chart (accepts numbers only)
  Waveform or XY plots
  X vs Y plots
  Spectrum and phase plots
  Labels and notepads


## Slide 15: OTHER IMPORTANT FEATURES
Custom Panel Views
Extensive plug-in card support
All blocks can have properties edited

## Slide 16: PANEL VIEW
Select the parts of your program you want the user to see (hold down control, click on blocks, then choose “Add to Panel”).
Edit properties of display features without changing the layout of the editing screen.
When saved as a runtime, this is all that is seen.
Have multiple panel views using the “show panel” and “hide panel” functions.

## Slide 17: PLUG-IN CARD SUPPORT
Full functionality of cards are supported.
Drivers and support for cards from numerous manufacturers.
Each function is represented in standard HP VEE format.
Many manufacturers also supplier higher level function blocks, to simplify programming.
Most manufacturers have their drivers available on their own pull down menu which appears when the drivers are installed.

## Slide 18: EDITING THE PROPERTIES OF BLOCKS
Click here or do a right mouse click over the block to get the menu specific to the block.
Select “edit properties”.
Modify the appearance of the block:
  Layout of data
  Colour
  Fonts
  Size
  Numerical format


## Slide 19: SPACE SAVING
Click here to reduce the space taken up by the block. Double click on a minimised block to expand it.
Bunch blocks together into “User Objects”, or “User Functions”. (The latter can be called from other parts of the program, and appears in the functions summary (explained earlier)
Remember - a user object or function will not output any data until completely finished. Its good to keep your program tidy, but make sure you don’t lose data.


## Slide 20: USEFUL HINTS… PLEASE READ
Never build a loop in a program without using a “Repeat” and a “Next” block. Drawing a line from the bottom of the program to the top with make it impossible for VEE to know where to start.
Any blocks without a data input or trigger input connected will run at the start of an HP VEE program and at no other time. This is therefore a constant.
There are two types of buttons: “OK” in the “flow” menu, and “button” in the “Data => Toggle control” menu. The latter often needs to have a reset control input added. With “OK”, decide whether you want in in-line or parallel to the rest of the program.

## Slide 21: Any Questions?
That was a whistle-stop tour of how HP VEE works.
If you have any technical or application questions or wish to order, please contact the UK Channel partner for HP VEE - Amplicon on (+44) 1273 570220